## Slide 3: Outline
Haar-feature based object detection algorithm
Custom design space exploration: Feature mapping problem
Experimental results

## Slide 4: Haar-Feature based object detection algorithm
Original image
Scaled images
(320 – 20) * (240 – 20) = 66,000 sub-windows
X axis
Y axis
0
240
320
Movement of sub-window
Faces detected on different scales
…
20x20
sub- window
Face found

## Slide 5: Face detection in sub-window
Fail
Pass
Facial Haar features
Calculate Haar-feature value:
Pixel_Sum(Rect_W) – Pixel_Sum(Rect_B)
Constant time Pixel_Sum calculation
Pixel_Sum(R1) =
P4 - P2 - P3 + P1 = 4
1 1 1
1 1 1
1 1 1
Original image
Integral Image
1 2 3
2 4 6
3 6 9
p1
p2
p3
p4
R1
Need 4 corner values
Stores Pixel sum of Rect(from top-left corner to this point)
P4
P2
P3
P1
20 x 20 sub-window

## Slide 6: Cascade decision process
Frontal-face has 2000 features
S1
2 features
S2
5 features
S3
16 features
S22
212 features
Divided into multiple stages
……
pass
pass
pass
Face detected
pass
Reject
Fail
Fail any stage will reject current sub-window

## Slide 7: Algorithm FPGA implementation
Buffer controller
Integral image
Rectangle
drawer
Video out
(objects in rectangles)
Classifier
Image scaler
20 x 20 Sub-window
Haar feature calculation/decision
Frame grabber
Video in
FPGA

## Slide 8: Integral image and Classifier
Frame grabber
Video in
Buffer controller
Integral image
Rectangle
drawer
Video out
(objects in rectangles)
Classifier
Image scaler
Classifier
Integral Image Buffer
(20 x 20 17-bit register file)
a1 a2 a3 a4
b1 b2 b3 b4
c1 c2 c3 c4
0
Feature threshold
>
Left value
Right value
Feature value
mux + multiply by constant
-1
x2
x2
x3
+(Feature sum)
Rect sum
Rect sum
Rect sum
Data delivery